## Slide 1: Enhancing Visual Inspection with Advanced Anomaly Detection Technologies
Jamal Saeedi
IDSIA, USI-SUPSI

## Slide 2: Visual inspection framework

## Slide 3: Data types and defects
Normal, defected, and annotated with segmentation map and class label.
Subtle descriptive defects vs. deviations from normality

## Slide 4: Pre-processing for tailored industrial solutions
Reducing variability, improving sensitivity, and integrating data for comprehensive defect analysis.
Image fusion
Contrast enhancement
Image alignment

## Slide 5: Learning algorithms
Normal samples
Defected samples
Test sample

## Slide 6: Zipper cursor anomaly detection
Data: zipper cursor images, trained on normal samples.
Algorithm: reconstruction-based method using autoencoder.
Challenges: detecting subtle defects on high resolution images.
Experimental setup with camera, lighting system and
holder and fixture
Training
Inference
Autoencoder
Trained Model
Reconstruction Error

## Slide 7: Car HVAC actuator inspection
Pilot station for image acquisition with 3 cameras plus lighting
Data: three views of HVAC actuators images, trained on normal samples.
Algorithm: feature embedding followed by machine learning-based anomaly detection
Challenges: environmental and material changes, low false negative ratio.

## Slide 8: Fabric textile defect detection and localization
Image acquisition setups, contact-based image sensor
Data: fabric textile image, trained on normal and synthetic samples.
Algorithm: generating synthetic defects to train a deep segmentation network.
Challenges: detecting and localizing subtle defects.

## Slide 9: Electrical discharge machined steel inspection
Data: EDA steel surface images, trained on labeled dataset.
Algorithm: Image processing-based region of interest (ROI) selection followed by CNN-based binary classifier.
Challenges: ROI selection and classifying ROIs with different aspect ratios.
+GF+ EDM die-sinking machine and the inspection system
ROI selection and classification

## Slide 10: Pipe inspection
Vision system with 4 line-scan cameras
Data: pipe surface image, trained on both labeled and annotated data.
Algorithm: anomaly detection followed by instance segmentation.
Challenges: high speed inspection (100 FPS), low false negative ratio, high number of defect classes.
Instance segmentation architecture

## Slide 11: Future works
Hybrid learning methods development
  Focus on combining discriminative and generative models
  Aimed at enhancing detection of subtle defects and deviations from normality
Collaboration with industrial partners
  Exploring new opportunities for collaboration
  Providing more efficient and adaptable solutions for the industry

## Slide 12: Contact
JAMAL SAEEDI, Ph.D.
Researcher, IDSIA, USI-SUPSI
Email: jamal.saeedi@idsia.ch
Phone: +41768307371
Alessandro Giusti, Ph.D.
Professor, IDSIA, USI-SUPSI
Email: alessandro.giusti@idsia.ch